RF Wireless Remote Control Kit (Model 0020526 S1PF-DC12+1CV-2-2)

Package Include:

1 x Receiver: S1PF-DC12

1x Transmitter: CV-2-2

1 x User manual

Features:

Application: It can be used in rolling blinds, rolling doors, projection screens, awnings, pumps, winches, conveyors or other appliances and equipments with DC motors, it can remote control DC motor rotates in the positive or reversal direction.

Wireless control, easy to install.

Waterproof: The receiver has waterproof case and waterproof connector, it can be installed outdoors.

You can rotate a motor in the positive or reversal direction with the transmitter (remote control) from any place within a reliable distance.

The RF wireless signal can pass through walls, floors and doors.

High Power: Each channel can work at maximum current 30A.

With limit control terminals: You can connect limit switches or sensors to stop the motor.

With wired control terminals: You can connect manual switches or external devices (with low level output signal, such as sensors) to control the motor.

You can turn on/ off the receiver with transmitter (remote control) from any place within a reliable distance.

Wireless RF signal can pass through walls, floors, doors or windows.

With reverse power protection and over current protection.

Reliable control: The receiver only works with the transmitter which use same code.

One/several transmitters can control one/several receivers simultaneously.

You can use two or more units in the same place.

Receiver Parameters:

Model No: S1PF-DC06 / S1PF-DC09 / S1PF-DC12 / S1PF-DC24

Control Mode: Momentary

Coding Type: learning code

Coding Setting: By learning

Power Supply (Operating Voltage): DC6V (S1PF-DC06), DC9V±1V (S1PF-DC09), DC12V±1V (S1PF-DC12), DC24V±1V (S1PF-DC24)

Output: DC6V (S1PF-DC06), DC9V±1V (S1PF-DC09), DC12V (S1PF-DC12), DC24V (S1PF-DC24)

Working Frequency: 315MHz/433MHz

Channel: 1 CH, can work with 1 DC motor

Static Current: ≤6mA

Maximum Working Current: 30A / each channel, so motor's maximum starting current can not exceed 30A.

PCB Size: 90mm x 59mm x 18mm

Case Size: 100mm x 68mm x 50mm

Work with Fixed code transmitters or Learning code transmitters.

Transmitters:

Model No.: CV-2-2

Shell Color: White

Channel/Button: 2

Button Symbol: ▲, ▼

Operating Voltage: 12V (1 x 23A -12V battery, can be used for 12 months)

Operating Current: 15mA

Operating Frequency: 315Mhz / 433Mhz

Encoding Chip: PT2262

Encoding Type: Fixed code by soldering, up to 6561 codes

Transmitting Distance: 500m / 1500ft (theoretically)

Modulation Mode: ASK

Operating Temperature: -20 ° C to +70 ° C

Unit Size: 110mm x 50mm x 18mm

Weight: 55g

Matching Transmitters:

This receiver can work with different transmitters. When you set the receiver in momentary mode, it should work with two button transmitters, such as model C-2 (100M), CWB-2 (50M, waterproof), CP-2 (500M), CV-2-2 (500M), or CB-2 (1000M) etc.

Working Range:

With a transmitter (such as CV-2-2) to form a complete set, the maximum working distance can reach 500M in an open ground.

The maximum working distance is a theoretical data, it shall be operated in an open ground, no barriers, no any interference. But in the practice, it will be hindered by trees, walls or other constructions, and will be interfered by other wireless signals. Therefore, the actual distance may not reach this maximum working distance.

If you want to have a further working range, you can install an external antenna to the receiver, and you also can use a powerful transmitter, such as CB series transmitters.

Usage (with transmitter CV-2-2):

Connect the positive pole of DC power supply to terminal “+” of INPUT, and connect the negative pole of DC power supply to terminal “-” of INPUT.

Connect terminals “OUTPUT” to motor. You can exchange motor's two wires to change the rotating direction of motor.

Press and hold button ▲: motor rotates in positive direction. Release button ▲: motor stops.

Press and hold button ▼: motor rotates in reversal direction. Release button ▼: motor stops.

Limit control terminals:

You can connect limit switches (normally open type) to terminals S1 and S2, and terminals S1 and S2 are normally open..

When motor rotates forward, if connect two terminals of S1, the motor will stop automatically.

When motor rotates reversal, if connect two terminals of S2, the motor will stop automatically.

Manual control terminals:

The receiver has manual control terminals, you can connect external devices, or sensors to control the receiver.

1) Signal input:

You can connect external devices (with low level output signal) to terminals 1 ( signal + ) and 2 ( signal - ), the external device’s output signal can control the receiver.

When the external device outputs low level signal to terminal 1 ( signal + ) and 2 ( signal - ), motor rotates in positive direction.

When the external device does not output signal to terminal 1 ( signal + ) and 2 ( signal - ), motor stops.

You can connect external devices (with low level output signal) to terminals 3 ( signal - ) and 4 ( signal + ), the external device’s output signal can control the receiver.

When the external device outputs low level signal to terminal 3 ( signal - ) and 4 ( signal + ), motor rotates in reversal direction..

When the external device does not output signal to terminal 3 ( signal - ) and 4 ( signal + ), motor stops.

2) The manual switches:

You can connect one manual switch to terminals 1 and 2,3 and 4, and then you can use this manual switch to control the receiver.

When connect terminals 1 and 2, motor rotates in positive direction

And when disconnect terminals 1 and 2, motor stops

When connect terminals 3 and 4, motor rotates in reversal direction

And when disconnect terminals 3 and 4, motor stops

How to pair the transmitter to the receiver:

1) Press the learning button of receiver for 1- 2 seconds; signal LED on the receiver is on. The receiver enters into status of LEARNING.

2) Press any one button on transmitter. If signal LED flashes quickly 15 times and turns off, it means learning is successful.

3) When receiver is in the status of LEARNING, press again the button of receiver, signal LED turns off, learning process will be discontinued.

4) The receiver can learn several remote controls with different codes.

Delete all transmitters:

We have learned remote control to the receiver. If you don’t want the receiver to work with the remote control, you can delete all codes of remote controls, which are stored in the receiver.

Operation: Press and hold the button of receiver until signal LED flashes slowly; release the button, LED keeps slow flash. That means all stored codes have been deleted successfully.

# Text boxes

## _

## _

## +

## +

External devices

Jumper-1

Jumper-2

# RF module

# Antenna

# IC

# Button

Signal LED

# DC Motor

## _

## +

# 4

# 2

# 3

# 1

# S2

# S1

# Status LED2

# M

# Power LED

Control DC Motor

# Relay2

# Relay1

# Status LED1

# INPUT

## _

## +

## DC Power Supply

# OUTPUT